## Slide 1: URS – UNIT-1
VIFI TEAM

## Slide 2: REGULATORY REQUIREMENT
The facility shall be designed to meet EU GMP/ UK-MHRA/TGA/MCC/TPT-Canada/Russian GMP

## Slide 3: DOSAGE AND FACILITY REQUIREMENTS URS
Facility shall be designed to accommodate contained transfer systems or material transfer systems for which ceiling height shall be minimum of 5 mts clear height (excluding Ducting and HVAC)
Separate primary entry for male/female and visitors shall be provided
The facility shall be designed for multiple products and unit operations separately so that operational constraints shall be avoided
Each unit operations shall have separate secondary changing facility
Facility shall be designed to cater following dosage forms,
  Granules/ Tablets/capsules (OSD)
    Blister (Alu-alu, Alu-PVDC, Alu-PVC,pelable foil)
    Bottle packing
  Pellets
    Bulk packing

## Slide 4: PRODUCTION CAPACITY
Tablets : 1.0 Billion units per annum (In total)
  Granulation-100lts suite for EB batches
  Granulation – 300lts suite for commercials
  Granulation – 500 lts suite for commercials
  Granulation – 1000 lts suite for commercials
  Granulation – Wruster 125 lts and 250 lts
  Separate blending area for capacity 30lts to 400lts (Bin blenders)
  Separate blending area for capacity 500lts to 2000lts (Bin blenders)
Capsules: 200 million units per annum
  Single and double pellets filling capability
  Tablets in capsules filling capability
Packing:
  Blister packing – 2 lines
  Bottle packing- 1 line
  Bulk packing (Pellets)- 1 line

## Slide 5: STORAGE AREAS
Ware house (RM)areas shall meet capacity planned
Sufficient FG storage area (With MLT of 7 days)
Capsules storage areas
Separate area for Printed packing materials & Tertiary packing materials
Dispensed Material storage areas (Day store)
WIP storage areas for Blend/Bulk Tablets/capsules
Documents storage for QA/QC
House keeping items storage areas
NOTE: All RM material ,Primary packing materials, FG goods,shall be stored in temperature NMT 25 deg

## Slide 6: QC FACILITY
Stability chambers –capacity (12000 lts X 4 conditions). 6000 lts x 3 for accelerated , intermediate and one standy.One photo stability chamber
Instrumentation Lab:
  HPLC – 24 Nos
  GC - 2
  Dissolution – 12 nos
  IR/UV and other instruments
Microbiology department with double door autoclave and culture handling
Balance room with connectivity
Cylinder storage and connectivity area with complete safety features
Fume hoods and hot room
Wet lab to cater volumes
Packing materials testing lab (separate)
Chemical storage area with ventilation
Control sample room (temperature of NMT 25 deg )
Sample storage area (allocation)
Cooling cambers for working standard storage
Chemical storage area with ventilation
Glass ware storage area
Washing area with drying facility
Seating capacity for 75 employeess

## Slide 7: UTILITY
Purified water systems with distribution loop to cater to all areas (manufacturing/WH/QC)with cold loop which shall meet USP standards
Boiler to meet planned capacity of production
Compressed air to meet required capacity and systems meets USP
HVAC shall be designed to have ISO 8/Class 100k. The areas shall be have suitable pressure differential to avoid cross contamination.
Filter cleaning booth for regular cleaning of filters
Effluent tanks for storage , which shall be sent out for treatment
Potable water tank to be provided to meet the proposed volumes

## Slide 8: SAFETY
Fire hydrant system shall be provided for the facility
Suitable fire alarm system shall be provided in all critical areas like Ware houses, stability, document rooms, manufacturing areas.
Scrap yard shall be designed to have safe disposal of scarp produced (glass/paper/plastic/powder/media/etc)
Shredder to be provided at scarp yard to make the printed packing materials/lables/etc to be shredded
QC area safety like shower, fire extinguisher

## Slide 9: General Areas
The facility shall have access for ambulace or fire engine to move around the facility with ease
The facility shall have no water logging within the facility
Conference Room: 25 seating capacity with projector and white board facility.
Wash rooms to cater for 250 employees (including contract manpower)- 150 males and 100 female
Bath rooms with hot water facility
Discussion rooms (4 seating capacity), 2 nos
Training room for 30 people
Creche: This is required as per the Factory rules, this shall cater to 10kids,2 maids and 1 supervisor.
Office space for 75 people (QA/RA/HR/SCM /IT/Cabins/Executive Directors cabin)
Document storage areas with CO2 purging facility
Dining facility for 100 people at a time
Scarp yard (Plastic/paper/glass/general waste)